## Slide 1: Automation Experience At THE RELATIVISTIC HEAVY ION COLLIDER
Christopher Zimmer
Brookhaven National Laboratory, Upton, NY USA

## Slide 2: Outline
-Overview of the RHIC complex
-Examples of automation types
-Need for automation
-Reasons why our methods of automation have been successful
-Perils of having many automated systems
-Automation’s effect on the skills of operators
-Training and skill retention
-Summary

## Slide 3
RHIC
LINAC
Booster
AGS
Tandems
STAR
PHENIX
EBIS
Overview of the RHIC Complex
NSRL
LINAC
EBIS
Tandems
Booster
NSRL
AGS
RHIC
STAR
PHENIX
-Two separate superconducting accelerators (‘blue’ and ‘yellow’ rings)
-2.4 miles in circumference (~3.8km)
-6 collision points, typically utilize 2

## Slide 4: Sequenced Automation Using TAPE
TAPE program is extremely versatile and widely used in the operation of our accelerators
  Generic automation tool
    Sequencing using a graphical editor
  Able to interact with controls devices, servers, applications and electronic log books
  Incorporates many traditional programming tools (variables, conditional statements, loops, etc.)
Although the application is in essence simplistic, it is a highly effective/flexible tool
TAPE (Tool for Automated Procedure Execution)

## Slide 5: Some Examples of TAPE Sequencer Usage
  Preparation of RHIC for ramping (instrumentation, RF, power supplies, triggers, etc.)
  Ramping RHIC to full energy
    Also putting the beams into collision
  Turning on/off hundreds of power supplies (access/power dip/quench)
  ‘Mode switching’
    Changing species in the injectors
  NSRL energy changes
  Documentation of running conditions
  General management over a large variety of systems
(with sequencing)

## Slide 6: Hard-coded Beam-based Correction Schemes
Automatic orbit correction in AGS
  Acquires an orbit and calculates the necessary correction
  User applies correction by simply pushing a button
Orbit and tune feedback in RHIC
  Continuous feedback loops that maintain the orbit/tunes at ideal values over the ramp duration
  Feedbacks can run at injection (before filling RHIC) to quickly optimize beam lifetime
Orbit feedback off
Tune feedback off
Orbit feedback on
Tune feedback on
Yellow Ring Horizontal Orbit RMS (Millimeters) Versus Ramp Time
(Multiple Ramps Shown)
Yellow Ring Betatron Tunes Versus Ramp Time
Qx
Qy
Qx
Qy
AGS Orbit Control Application

## Slide 7: Other Code-driven Beam-based Corrections
Stochastic cooling in RHIC
  Decreases the beam emittance in all three planes (H, V, L)
    Uses a sophisticated pickup/kicker arrangement to measure and mitigate the diffusion of particles
  Increases collisions by factor 2-5
Automated optimization of collision steering in RHIC
  Implements minor steering adjustments using the collision rate as a figure of merit
  Steers multiple interaction regions in parallel
  Especially important with the advent of stochastic cooling
Collision Rate Versus Time (Uranium Beam)
Integrated collisions increased by factor of five!
lisa (Luminosity and IR Steering Application)

## Slide 8: User Controlled Access at NSRL
Fully automated access system
  Controls entry/exit from the target exposure room
    MCR operators used to perform this task
  When an entrance is requested, system places area into a controlled access state and prevents the delivery of beam
  User obtains an RFID key from iris scanner
  System accounts for entry/exit of each person using an arrangement of optical turnstiles and RFID antennas
  Restores the beam after access
UCA Interface
Outside entrance gate to target exposure area
Interior of entrance gate with automated personnel accounting equipment

## Slide 9: Automation is Necessary!
Preparing for and executing a RHIC ramp necessitates hundreds of verifications/initializations/triggers
  Impractical and susceptible to human error
Mode switching sequence provides quick (~2 minutes!) and reliable reconfiguration of the injector chain for running different species
NSRL has a need for rapid and consistent energy changes
Controlling hundreds of power supplies easily managed with TAPE
Orbit/tune feedback has a profound effect on RHIC setup time
  Only takes 1-2 test ramps to reach full energy with a new species
  Enables running of several species, increases time in collision
Stochastic cooling provides an incredible benefit, but is complex
User Controlled Access for NSRL has been a huge success, and has freed operators from performing a very menial and repetitive task

## Slide 10: Our Sequenced Automation Method Works Well
The simplicity of our sequencing application is a key to its success
The barrier for understanding, creating and modifying automation schemes using TAPE is low
  Steps are clearly laid out
  Anyone can understand the steps
  Proficiency in code-writing not required to create or modify scripts
Almost any repetitive task can be automated using TAPE

## Slide 11: Issues With Sequenced Automation
Steps can and do fail. The error messages given by the application are at times arcane
  Error messages could be more informative
If the application freezes/crashes, there can be confusion as to what steps were executed
  Every step is logged which aids in diagnosis, but the abnormal machine state can be tricky
Ease of running a sequence (single button click) can lead to inadvertently running the wrong sequence
  Operators must exercise caution

## Slide 12: Issues With Other Automation Types
RHIC beam-based feedback systems were implemented by a single person, and are only understood by that person
  Single point of failure
  We rely on these systems heavily, they have become essential
Stochastic cooling is another black box
  Very few people understand how the system works
  It also occasionally gets into a bad state, increases emittance
User Controlled Access at NSRL
  Susceptible to hardware faults, coding errors and loose wires
    Multiple issues when system first brought online, better now
    Necessary byproducts of commissioning

## Slide 13: Does Automation Hurt the Operators?
The consensus among our group is that automation, when properly executed, does not by virtue significantly deteriorate operational skills
  Automation undoubtedly gives the operators less tasks to execute, but…
    Many automated tasks are monotonous and require little skill
      Automating tedious tasks improves quality of life for operators

## Slide 14: Does Automation Hurt Operators (2)?
Our sequencing utility improves operator creativity/skills
  Encourages improvement of automation schemes
  Application is a window to the controls system
Large majority of tuning and troubleshooting still done by hand
Proficient operators will usually understand what automation of skilled tasks accomplishes and can execute those tasks
  Assuming that the automation is transparent

## Slide 15: Necessary Supplements to Automation
Automation certainly fosters an environment where it can be more difficult to obtain/retain certain skills
  As automation encroaches more upon skilled (typically human-driven) accelerator troubleshooting and tuning activities, the negative effects will become more pronounced
    Accelerators that tune and fix themselves?
Negative effects on operator competency seem to correlate with an opaque automation scheme and/or a lack of accompanying education/training
Automation must be supplemented with regimented training and hands on experience

## Slide 16: Imparting and Retaining Skills
We administer lecture-styled training on a variety of topics
Our group also requires the passing of ‘practical exams’
  Hands on test of troubleshooting ability
  Sr. operator ‘breaks’ machine(s), jr. operator fixes problems with machine(s)
  Some practicals involve demonstrating competency in an automated task
    NSRL energy change

## Slide 17: Skill Retention With Automation
We could do better to ensure understanding of automated tasks
  Limited number of practical exams
    No mode switching practical, no recertification exams
  Formal training courses are lacking; we rely more on informal training while on shift
  “Push the magic button and call me if it fails” needs to be avoided
    Instead of fielding calls when system breaks, teach operators about system

## Slide 18: Summary
Any task that can be reliably automated should be
  Leads to more efficient operation and reduces human error
  We have yet to see a glaring example of too much automation
  Automation works quite well for us, with a few caveats
Automation needs to be as transparent as possible
  Not every automation scheme can be perfectly transparent
  Better dissemination of information in those cases
Use of automation should ideally be accompanied (even preceded) by a demonstration that the user understands the fundamentals of the task and is able to execute the task
  Don’t give a child a calculator to divide numbers without first teaching them long division; they need to be able to divide by hand if the calculator breaks!
A solid foundation of training along with continuing education is a necessary supplement to automation
  Operators and support personnel can proactively minimize the possible negative effects of automation