## Slide 1: SLAC workshop 7-10 July 2009 WP1: microwave-based accelerators Progress towards a new standard X-band high-power flange
G. Riddone, 08.07.2009
(contribution from C. Garion)

## Slide 2: Outline
General requirements
Recall of existing design from SLAC
Presentation of the new design
Program

## Slide 3: Requirements
Reliable joint - high sealing performance
Smooth flange-gasket-flange transition (RF performance)
Simple shapes and preferably symmetrical joint
Easy assembly
Cheap production
Needs
  X-band test stands (few hundreds): needs for CERN and for several other test stands (eg. PSI. Elettra,..)
  CLIC - about 500 000 units

## Slide 4: SLAC design
gasket
flange
flange
Parts
Two different flanges - 2 stainless steel WR90 flanges (AISI316LN)
1 OFE copper gasket
Observations:
- Not symmetrical gasket cross-section
- Main sealing mechanism comes from shearing not compression
flanges clamped with 8 bolts
Gasket
Flanges

## Slide 5: Some remarks on SLAC design
Large and non constant displacements into gasket aperture
0.25
0.25
Lateral profile of the maximum inner displacements
Contact pressure between upper gasket surface and flange
Contact pressure between lower gasket surface and flange
No sealing
Sealing
No sealing
Sealing
Different contact pressure distribution for upper and lower surface of the gasket
Trapped volume
Trapped volume

## Slide 6: CERN design proposal
Symmetry
Assembled joint
gasket
flange
New CLIC design concept
Same flanges
Rectangular cross section OFS copper gasket
Symmetrical, “knife” based design
Initial gasket position away from flange/flange plane
AISI316LN flanges with 6 bolts and 2 centering pins

## Slide 7: Some advantages on CERN design proposal
Homogeneous contact pressure –symmetric type joint
Cheaper production – simple and easy to machine gasket shape and one type of flange only
Easier assembly – symmetric, self-placed gasket with additional pins centering joint system
Better properties – smooth flange-gasket-flange transition
SYMMETRY
NO SYMMETRY
New proposal
SLAC design
2)
3)
1)
1)
1)
2)
Female flange
Gasket with moderate shape
Male flange
One type of flange
Gasket with simple shape
self-placed
gasket
self-placed
gasket
+
Pins centering
joint system
0.25 mm
0.15 mm
Flange
Flange
Gasket
< 0.1 mm
Flange
Flange
Gasket

## Slide 8: CERN design optimization
Geometrical parameters
a (Q1)
b (Q2)
thickness
Initial
position
flange
gasket
Optimization of the joint geometrical parameters based on FE models:
Flange: knife (a,b), thickness, diameter, type and number of bolts
Gasket: thickness, width
Interface: imprint depth, initial position
Criteria:
Leak rate (<10-12 mbar·l/s)
P = contact pressure, w= contact width, A, R = parameters as a function of roughness
Plastic strain in the flanges
Cost

## Slide 9: CERN design optimization
The displacement into aperture is an input for future RF calculations
Displacement into the aperture

## Slide 10
CERN Proposal Flange Drawing

## Slide 11: Program
Circular gasket design: leak rate measurements
Final design: 5 full units (CINEL) available at CERN as well as gaskets
  Dimensional control  conform
  Leak-rate measurement as a function of torque (promising results)
  Realization of the tooling for centering the gasket (done)
  Displacement as a function of torque
  Low-power RF tests at CERN
  Preparation for high-power testing at SLAC of two units: Sept 09