## Slide 1: T18_VG2.4_Disk_#2 processing summary
SLAC Workshop
090708-10
T. Higo and Nextef group

## Slide 2: Whole history of T18_#2 processing
Installation in Oct. 2008
Steady-state run at 80MV/m in Dec. 2008
Higher field in Jan-Feb 2009
Breakdown rate meas. in Mar.-Apr. 2009
Longer pulse in latter half of Apr. 2009
Breakdown rate meas. May 2009
Various measurement in June 2009
Finish with 4000 hrs operation

## Slide 3: Processing history for 9 months Nextef startup and careful processing

## Slide 4: Recovery pass in (T,P) space
CERN
T
P
50%P, -20%T
SLAC
T
P
20%P, 20nsT
KEK
T
P
aP, -1stepT
In case of number of BD’s even at lower power level than defined

## Slide 5: Whole BD history of T18_VG2.4_Disk #2

## Slide 6: Nextef: RF monitors along waveguide
Two klystrons
ACC Structure
Low loss waveguide
2-klystrons  120MW, 300ns
klystron—3dB 2.3m
3dB— LLWG 1.5m
LLWG 5m
LLWG—ACC Str 5.0m
WR90 flanges ~36sets*7mm SUS
Loss Kly.Str. ~23%
Delay ~ 50ns
S+N
ACC-IN
S
N
Tr
Rs
Ra

## Slide 7: Nextef: Monitors along beam axis
FC-Mid
FC-UP
FC-DN
Qmass
PM
PM
AM
GV
GV
ACC str

## Slide 8: Now T18_VG2.4_Disk #2 has been processed since late October
T18_VG2.4_Disk
GV
SLAC
3dB hybrid
Acoustic
sensors
Plastic scintilator
& PMT
FC
(These are not used effecively.)

## Slide 9: Big breakdown followed by a breakdown from the very first pulse
file number= 3 20081124_210211_1 Red=final, black=previous pulse and blue=-2nd pulse
file number= 4 20081124_210301_1 Red=final, black=previous pulse and blue=-2nd pulse
1st pulse BD, following big BD
Nominal BD
Fs
Rs
Ra
Tr
FC-UP
FC-Mid
Fs
DPO1
DPO2

## Slide 10: Current burst toward upstream
Rare event but need to understand the mechanism
One out of 100 breakdowns
Abrupt big burst in current only to upstream
no change in RF pulse shape
Fs
Rs
Ra
Tr
FC-UP
FC-Mid
Fs

## Slide 11: Power at BD’s and BDR during 27 days at 80MV/m (35MW) during RF-ON from 700 ~ 1200 hours since startup
BDR
~17 str. BD / 566 hr
~0.030 BD/hr/str
~0.75 x10-6 BD/Pulse/m
Finished at 9:00 on Dec. 25
Started at 10:00 on Nov. 28
566 hrs run / 643 hrs
= 88% ON

## Slide 12: 252ns, 65MW
Total operation hours >5MW = 140.6 hours
Period ACC-IN > 64 MW = 91.7 hours

## Slide 13: Appearance of breakdowns at 65MW run

## Slide 14: 252ns, 70MW

## Slide 15: Appearance of breakdowns at 70MW run

## Slide 16: 252ns, 75MW

## Slide 17: Appearance of breakdowns at 75MW run

## Slide 18: Typical processing / steady-state run
Breakdowns are
  mostly followed by a few to several successive breakdowns
  typically from the very first pulse at even lower power.
Spurious events exist
  with flush of current towards upstream occur from time to time

## Slide 19: Breakdown rate evaluation
It is not so clear from this experiment that the breakdown rate decreases as function of “processing.”

## Slide 20: Breakdown rate versus Eacc
Exponential fit.

## Slide 21
Power fit.
Cannot discuss functional form due to large scatter.

## Slide 22
100
150
200
10
-7
10
-6
10
-5
10
-4
RF Flat Top Pulse Width: ns
BKD Rate: 1/pulse/m
RF BKD Rate Gradient Dependence for 230ns Pulse at Different Conditioning Time
After 250hrs RF Condition
After 500hrs RF Condition
After 900hrs RF Condition
RF BKD Rate Pulse Width Dependence at Different Conditioning Time
G=108MV/m
G=108MV/m
G=110MV/m
RF Processing of the T18 Structure
After 1200hrs RF Condition
This performance maybe good enough for 100MV/m structure for a warm collider, however, it does not yet contain all necessary features such as wake field damping. Future traveling wave structure designs will also have better efficiencies
R. Ruth at X-band workshop at CI, UK, Dec. 2009

## Slide 23: Breakdown rate versus width
Not enough to discuss functional form.
But it is evident that the longer pulse makes breakdown rate large with much more than linear dependence.

## Slide 24: Summary of breakdown rate
Exponential slope as Eacc
  Data scattering band around a slope is by an order of magnitude
  Slope = an order of magnitude by 10 MeV/m
  Not enough to discuss about the functional form
Breakdown rate evolution
  Reduction of BDR was not seen in last 2000 hours

## Slide 25: Breakdown position and timing
Still trying to analyze in detail.
At present, mainly refer to Steffen’s previous analysis
  More frequent at downstream

## Slide 26: Analysis still on the way 137 examples of run24: 60MW, 400ns
Timing of Rs rise and Tr fall show correlation.
Two cases: those at the same time and those at 50ns later.
Position and time of the breakdown should be deduced from Rs and Tr.
FC current burst timing and amount should be integrated in the analysis.
Breakdowns from the very first pulse are missing; should be included in the analysis.

## Slide 27
Red real cell timing, blue linear cell timing, 205 ns data
Breakdown position for 205 ns data
Steffen 090227

## Slide 28: Dark current measurement
Setup
Amount and beta value of dark current versus processing time
Spectrum at RF-ON 2000hrs and 4000hrs
75cm
75cm
195cm
FC-DN
FC-UP
FC-Mid
AM

## Slide 29: Amount of dark current
FC-Mid = 30mA
@100MV/m
FC-UP ~ FC-Mid/3
FC-DN ~ FC-Mid/4

## Slide 30: Dark current evolution 252nsec
Measured at RF ON 700 – 1200 – 2100 – 3000 – 3400 hours
Decreased by a factor 2 between processing with max Eacc 80  110MV/m,
but no more suppression in the following steady-state run for more than 1000 hours

## Slide 31: Dark current evolution 252nsec
Measured at RF ON 700 – 1200 – 2100 – 3000 – 3400 hours
No big change in shape nor slope (beta).

## Slide 32: Deduction of the field enhancement factor
f(Cu)=4.52eV
Assuming Es/Eacc=2
actually T18_VG2.4_Disk
Es/<Eacc>~2.62 max
Fitting of modified F-N curve

## Slide 33: Width dependence
Upstream current behaves as linear on width
Downstream current has two components.

## Slide 34: Dark current spectra in June
Dependence on power
Dependence on width
Actual field of analyzer magnet was checked.
The formula used up to now pc[MeV/m] = 1.646 x I [A] = 8.23xRef. Volt. [V] was confirmed.
Two peaks appear and higher for higher momentum one.
Less than ½ of full acceleration.
Little exists below 2.5MeV/m.

## Slide 35: Dark current versus operation frequency
Increase as operation frequency increases.
Easy to be captured for both!?

## Slide 36: Dark current behaviour
Amount
  to upstream << to downstream
  Divergent: 1/4 from Mid to DN
  Linear vs pulse width
Reduction of dark current
  By a factor 2~3 during first 2000 hrs
  No reduction after 2000 hrs
Beta value
  Stayed almost constant from 700hrs to 3300 hrs
  Not processed?
Spectrum
  Two peaks below half of full acceleration

## Slide 37: Conclusion
Established a basic procedure of processing and evaluation
  Can proceed a series of structure tests
  Better to further develop a system in such as
    Phase measurement, missing energy evaluation, etc.
Breakdown rate was evaluated.
  Gross comparison with that of SLAC is consistent with each other.
  In order to precisely compare, power estimation and identification of breakdowns should be better.
Dark current
  Decreased during initial processing but stayed constant during a long-term run without higher field nor longer pulse processing.
  Energy is at most a half of full acceleration and little exists below a few MeV/c.
Breakdown pulse analysis
  Breakdown pulses are still to be analyzed carefully.